## Slide 1: CSE 460: VLSI Design (Lab)
Experiment 3 (Example)
with Mealy and Moore Type

## Slide 2: Finite State Machine
In Combinational logic circuits, outputs are determined solely by the present values of the inputs.
In Sequential circuits, outputs depend both on the past behavior of the circuit and the present values of the inputs. The storage elements in terms of flip-flops can reserve the state information of the logic circuit at any given time.
The sequential circuits in which a clock signal is used to control the operation of the circuit, is called synchronous sequential circuits. These synchronous sequential circuits are known in general as Finite State Machines (FSMs).
The building blocks of a finite machine are combinational circuits and one or more flip-flops. Under the control of the clock signal, the flip-flops change their state as determined by the combinational logic.
Combinational
circuit
Combinational
circuit
Flip-flops
W
Clock
Z
Q

## Slide 3
FSMs can be of two types:
Moore type FSM
  The sequential circuits whose outputs depend only on the states of the circuit are of Moore type.
Mealy type FSM
  The sequential circuits whose outputs depend on both the state and the present primary inputs are of Mealy type
Combinational
circuit
Combinational
circuit
Flip-flops
W
Clock
Z
Q
Finite State Machine

## Slide 4: Moore Type FSM
Problem:
Suppose that we wish to design a circuit that meets the following specification:
  The circuit has one input, w, and one output, z.
  All changes in the circuit occur on the positive edge of a clock signal.
  The output z is equal to 1 if during two immediately preceding clock cycles the input w was equal to 1. Otherwise, the value of z is equal to 0.
Input-output combination:

## Slide 5: Moore Type FSM
Figure : State Diagram
Present State | Next State |  | Output z
 | w=0 | w=1 | 
A | A | B | 0
B | A | C | 0
C | A | C | 1
Figure : State Table

## Slide 6: Moore Type FSM
Figure : State Diagram
Present State | Next State |  | Output z
 | w=0 | w=1 | 
00(A) | 00(A) | 01(B) | 0
01(B) | 00(A) | 10(C) | 0
10(C) | 00(A) | 10(C) | 1
11 | Dd | dd | d
 | Next State |  | Output z
 | w=0 | w=1 | 
00(A) | 00(A) | 01(B) | 0
01(B) | 00(A) | 10(C) | 0
10(C) | 00(A) | 10(C) | 1
11 | Dd | dd | d

## Slide 7: Moore Type FSM
Present State | Next State |  | Output z
 | w=0 | w=1 | 
00(A) | 00(A) | 01(B) | 0
01(B) | 00(A) | 10(C) | 0
10(C) | 00(A) | 10(C) | 1
11 | dd | dd | d
 | Next State |  | Output z
 | w=0 | w=1 | 
00(A) | 00(A) | 01(B) | 0
01(B) | 00(A) | 10(C) | 0
10(C) | 00(A) | 10(C) | 1
11 | dd | dd | d

## Slide 8: Moore Type FSM

## Slide 9: Mealy Type FSM
Problem:
We wish to design a circuit that meets the following specification:
  The circuit has one input, w, and one output, z.
  All changes in the circuit occur on the positive edge of a clock signal.
  The output z is equal to 1 if during two immediate clock cycles the input w was equal to 1. Otherwise, the value of z is equal to 0.
Input-output combination:

## Slide 10: Mealy Type FSM
Figure : State Diagram
/
/
/
/
Present State | Next State |  | Output z | 
 | w=0 | w=1 | w=0 | w=1
A | A | B | 0 | 0
B | A | B | 0 | 1
Figure : State Table

## Slide 11: Mealy Type FSM
Figure : State Table
Present State | Next State |  | Output z | 
 | w=0 | w=1 | w=0 | w=1
A | A | B | 0 | 0
B | A | B | 0 | 1
Figure : State-assigned Table
Present State | Next State |  | Output z | 
y |  |  |  | 
 | w=0 | w=1 | w=0 | w=1
 | Y | Y |  | 
0(A) | 0(A) | 1(B) | 0 | 0
1(B) | 0(A) | 1(B) | 0 | 1

## Slide 12: Mealy Type FSM
Present State | Next State |  | Output z | 
y |  |  |  | 
 | w=0 | w=1 | w=0 | w=1
 | Y | Y |  | 
0(A) | 0(A) | 1(B) | 0 | 0
1(B) | 0(A) | 1(B) | 0 | 1

## Slide 13: Mealy Type FSM

## Slide 14: An Example
Problem: Derive the state diagram for an FSM that has an input w and an output z. The machine has to generate z = 1 when the previous four values of w were 1001 or 1111; otherwise, z = 0.Overlapping input patterns are allowed. An example of the desired behavior is
Clock cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
w | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1
z | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0

## Slide 15
State diagram(Moore type)

## Slide 16
Present State | Next State |  | Output z
 | w=0 | w=1 | 
S0 | S0 | S1 | 0
S1 | S5 | S2 | 0
S2 | S5 | S3 | 0
S3 | S5 | S4 | 0
S4 | S5 | S4 | 1
S5 | S6 | S1 | 0
S6 | S0 | S7 | 0
S7 | S5 | S2 | 1
Figure : State Table
Present State | Next State |  | Output z
 | w=0 | w=1 | 
000(S0) | 000(S0) | 001(S1) | 0
001(S1) | 101(S5) | 010(S2) | 0
010(S2) | 101(S5) | 011(S3) | 0
011(S3) | 101(S5) | 100(S4) | 0
100(S4) | 101(S5) | 100(S4) | 1
101(S5) | 110(S6) | 001(S1) | 0
110(S6) | 000(S0) | 111(S7) | 0
111(S7) | 101(S5) | 010(S2) | 1
 | Next State |  | Output z
 | w=0 | w=1 | 
000(S0) | 000(S0) | 001(S1) | 0
001(S1) | 101(S5) | 010(S2) | 0
010(S2) | 101(S5) | 011(S3) | 0
011(S3) | 101(S5) | 100(S4) | 0
100(S4) | 101(S5) | 100(S4) | 1
101(S5) | 110(S6) | 001(S1) | 0
110(S6) | 000(S0) | 111(S7) | 0
111(S7) | 101(S5) | 010(S2) | 1
Figure : State-assigned Table
State table (Moore type)

## Slide 17: State assigned table (Moore Type)
Present State | Next State |  | Output z
 | w=0 | w=1 | 
000(S0) | 000(S0) | 001(S1) | 0
001(S1) | 101(S5) | 010(S2) | 0
010(S2) | 101(S5) | 011(S3) | 0
011(S3) | 101(S5) | 100(S4) | 0
100(S4) | 101(S5) | 100(S4) | 1
101(S5) | 110(S6) | 001(S1) | 0
110(S6) | 000(S0) | 111(S7) | 0
111(S7) | 101(S5) | 010(S2) | 1
 | Next State |  | Output z
 | w=0 | w=1 | 
000(S0) | 000(S0) | 001(S1) | 0
001(S1) | 101(S5) | 010(S2) | 0
010(S2) | 101(S5) | 011(S3) | 0
011(S3) | 101(S5) | 100(S4) | 0
100(S4) | 101(S5) | 100(S4) | 1
101(S5) | 110(S6) | 001(S1) | 0
110(S6) | 000(S0) | 111(S7) | 0
111(S7) | 101(S5) | 010(S2) | 1

## Slide 18: Timing diagrams (Moore Type)
Figure : Output waveform

## Slide 19: An Example
Problem: Derive the state diagram of the Mealy version for the example FSM that is, the FSM will generate at the instant the input values of have the pattern or . Overlapping of the input patterns are allowed.
Clock cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
w | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1
z | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1

## Slide 20
/
/
/
/
/
/
/
/
/
/
/
/
State diagram(Mealy type)

## Slide 21
Present State | Next State |  | Output z | 
 | w=0 | w=1 | w=0 | w=1
S0 | S0 | S1 | 0 | 0
S1 | S4 | S2 | 0 | 0
S2 | S4 | S3 | 0 | 0
S3 | S4 | S3 | 0 | 1
S4 | S5 | S1 | 0 | 0
S5 | S0 | S1 | 0 | 1
Figure : State Table
Present State | Next State |  | Output z | 
 | w=0 | w=1 | w=0 | w=1
000(S0) | 000(S0) | 001(S1) | 0 | 0
001(S1) | 100(S4) | 010(S2) | 0 | 0
010(S2) | 100(S4) | 011(S3) | 0 | 0
011(S3) | 100(S4) | 011(S3) | 0 | 1
100(S4) | 101(S5) | 001(S1) | 0 | 0
101(S5) | 000(S0) | 001(S1) | 0 | 1
 | Next State |  | Output z | 
 | w=0 | w=1 | w=0 | w=1
000(S0) | 000(S0) | 001(S1) | 0 | 0
001(S1) | 100(S4) | 010(S2) | 0 | 0
010(S2) | 100(S4) | 011(S3) | 0 | 0
011(S3) | 100(S4) | 011(S3) | 0 | 1
100(S4) | 101(S5) | 001(S1) | 0 | 0
101(S5) | 000(S0) | 001(S1) | 0 | 1
Figure : State-assigned Table
State table (Mealy type)

## Slide 22: State assigned table (Mealy type)
Present State | Next State |  | Output z | 
 | w=0 | w=1 | w=0 | w=1
000(S0) | 000(S0) | 001(S1) | 0 | 0
001(S1) | 100(S4) | 010(S2) | 0 | 0
010(S2) | 100(S4) | 011(S3) | 0 | 0
011(S3) | 100(S4) | 011(S3) | 0 | 1
100(S4) | 101(S5) | 001(S1) | 0 | 0
101(S5) | 000(S0) | 001(S1) | 0 | 1
 | Next State |  | Output z | 
 | w=0 | w=1 | w=0 | w=1
000(S0) | 000(S0) | 001(S1) | 0 | 0
001(S1) | 100(S4) | 010(S2) | 0 | 0
010(S2) | 100(S4) | 011(S3) | 0 | 0
011(S3) | 100(S4) | 011(S3) | 0 | 1
100(S4) | 101(S5) | 001(S1) | 0 | 0
101(S5) | 000(S0) | 001(S1) | 0 | 1
Figure : State-assigned Table
Figure : Verilog code (part 1)
Figure : State-assigned Table

## Slide 23: State assigned table (Mealy type)
Present State | Next State |  | Output z | 
 | w=0 | w=1 | w=0 | w=1
000(S0) | 000(S0) | 001(S1) | 0 | 0
001(S1) | 100(S4) | 010(S2) | 0 | 0
010(S2) | 100(S4) | 011(S3) | 0 | 0
011(S3) | 100(S4) | 011(S3) | 0 | 1
100(S4) | 101(S5) | 001(S1) | 0 | 0
101(S5) | 000(S0) | 001(S1) | 0 | 1
 | Next State |  | Output z | 
 | w=0 | w=1 | w=0 | w=1
000(S0) | 000(S0) | 001(S1) | 0 | 0
001(S1) | 100(S4) | 010(S2) | 0 | 0
010(S2) | 100(S4) | 011(S3) | 0 | 0
011(S3) | 100(S4) | 011(S3) | 0 | 1
100(S4) | 101(S5) | 001(S1) | 0 | 0
101(S5) | 000(S0) | 001(S1) | 0 | 1
Figure : State-assigned Table
Figure : Verilog code (part 2)

## Slide 24: Timing diagrams (Mealy Type)
Figure : Output waveform